## Slide 1
3.6 Data transfer Instructions
The XCHG instruction
Supposing AX=1234H, BX=5678H
XCHG AX, BX
After execution of XCHG, BX=1234H, AX=5678H
The BSWAP instruction (486+ only)
EAX before...
…and after execution of BSWAP EAX

## Slide 2
3.6 Data transfer Instructions
The LEA instruction
Examples:
LEA SI, [200H]
The second operand specifies the memory location at the address 200H, so value 200H is loaded into SI
MOV SI, [200H]
The second operand specifies the memory location at the address 200H, so the content of memory locations at address 200H and 201H is loaded into SI
LEA SI, [DI+BX+5H]
Value 1025H is loaded into SI.
Supposing (BX=20H, DI=1000H):
The XLAT instruction
Example:
Supposing BX=200H, AL=4, DS=100H,
Mem(1204H)=55H.
XLAT
After XLAT, AL=55H

## Slide 3
3.6 Data transfer Instructions
The LDS, LES, LFS, LGS, LSS instructions
Example:
LDS SI, [200H]
The content of memory 200H and 201H is loaded into SI, and the content of memory 202H and 203H is loaded into DS.
Example:
LSS ESP,FWORD PTR NEWSTACK
The content of memory from address NEWSTACK to NEWSTACK+5 is loaded into ESP and SS.

## Slide 4
3.6 Data transfer Instructions
Assembler directives BYTE PTR, WORD PTR,
DWORD PTR, FWORD PTR, OFFSET, SEG and DF
BYTE PTR = byte pointer => the operand is a byte at the specified address in memory
WORD PTR = word pointer => the operand is a word at the specified address in memory
DWORD PTR = double word pointer => the operand is a double word at the specified address in memory
FWORD PTR = far word pointer => the operand is a far word pointer at the specified address in memory (the four bytes at lower addresses specifying the offset and the other two bytes specifying the segment)
DF =define far word => reserves memory space and define such a far word pointer (similar to DB)
When the operand in memory was defined using DB, DW, DD or DF, the directives above are useless.
OFFSET => the operand the offset of the specified address in memory
SEG = segment => the operand the value of the segment used to declare the specified data
Examples:
MOV WORD PTR [SI],5
The 16-bit value 5 is loaded into memory at the address specified by DS:SI.
LEA DX, MESSAGE
MOV DX, OFFSET MESSAGE
The same effect , but MOV instruction is faster and shorter
MOV AX, SEG MESSAGE
MOV DS, AX
Identify the segment used when declared data MESSAGE, and load its value in DS (in two steps).