## Slide 1
3.7 String Instructions
Specifying the Operands’ Size and Address and the String Direction
STRING = a data collection in memory.
String ELEMENTS can be: bytes (8-bit), words (16-bit), or double-words (32-bit).
A SOURCE STRING and a DESTINATION STRING can be specified.
The CURRENT ELEMENT in the SOURCE STRING is pointed by DS:[E]SI.
The CURRENT ELEMENT in the DESTINATION STRING is pointed by ES:[E]DI.
A STRING INSTRUCTION operates by default on current elements in the Source String and in the Destination String or only one of them. The operands don’t need to be specified for String Instructions, unless their size (byte, word, double-word) has to be specified this way.
A simplified way to specify the operands’ size is to add suffix B, W or D to Mnemonic.
Executing a STRING INSTRUCTION, the implied Index Registers ([E]SI, [E]DI or both) are automatically updated to point the next element in the string, which becomes the CURRENT ELLEMENET for the next STRING INSTRUCTION involving the same String. The update means increment or decrement the Index Register content by byte count of the string element. (1 if the elements are bytes, 2 for word elements, and 4 if the elements are double-words).
The DIRECTION of pointer updating is imposed by the DF (Direction Flag) in FLAGS register:
[E]SI and/or [E]DI are incremented if DF=0, or decremented (if DF=1).
Examples:
DI  DI+4*(-1)DF
After a String Instruction implying a double-word Destination String
SI  SI+(-1)DF
After a String Instruction implying a byte Source String
Setting Direction Flag:
CLD ;clear DF = auto-increment
STD ;set DF = auto-decrement

## Slide 2
3.7 String Instructions
The MOVS instruction
Moves an element from the source string in the destination string. Increase or decrease (depending on DF) both [E]SI and [E]DI by the byte-count of the operands.
The CMPS instruction
Performs the subtraction (ES:[E]DI)-(DS:[E]SI), doesn’t store the result, but sets flags accordingly. Increase or decrease (depending on DF) both [E]SI and [E]DI by the byte-count of the operands.

## Slide 3
3.7 String Instructions
The SCAS instruction
Performs the subtraction AL-(ES:[E]DI) or AX-(ES:[E]DI) or
EAX-(ES:[E]DI), doesn’t store the result, but sets flags accordingly. Increase/decrease only [E]SI.
Load (move) into AL or AX or EAX the content of the memory location pointed by (DS:[E]SI). Increase/decrease only [E]SI.
The LODS instruction
Store (move) the content of AL or AX or EAX to the memory location pointed by (ES:[E]DI). Increase/decrease only [E]DI.
The STOS instruction

## Slide 4
3.7 String Instructions
The INS instruction
Input port address is always expressed register indirect using DX (16 bits).
The OUTS instruction
Output port address is always expressed register indirect using DX (16 bits).
The source is the memory location addressed by [E]SI. A byte, a word or a double word can be output. After output, [E]SI is automatically incremented (or decremented - depending on the direction flag DF) by 1, 2 or 4.
The destination is the memory location addressed by ES:[E]DI. A byte, a word or a double word can be input. After input, [E]DI is automatically incremented (or decremented - depending on the direction flag DF) by 1, 2 or 4.

## Slide 5
3.7 String Instructions
The REP, REPE/REPZ, REPNE/REPNZ prefixes
Each string instruction acts on a single element in a source string and/or on a single element in the destination string. To operate on the whole source and/or destination string, a repetitive execution is needed. Loop and Jump instructions allow repeating of a group of instructions (a program sequence). The REP prefix allow a single instruction to be repeated.
The value in [E]CX (before execution of the instruction with REP prefix) specifies how many times the instruction is executed. (If [E]CX=0 before REP prefix arrived, the instruction is skipped (not executed). Each iteration decrements [E]CX until it arises at 0. The repetition is stopped and the next instruction is executed.
REPE (REPeat while Equal) is identical to REPZ (REPeat while Zero) (Same code with two different mnemonics). Additional to REP, this instruction verifies ZF (Zero Flag in FLAGS) and stops repetition when ZF=0.
Decrementing [E]CX doesn’t affect any flags!
Similarly, REPNE (REPeat while Not Equal) is identical to REPNZ (REPeat while Not Zero) (Same code with two different mnemonics). Additional to REP, this instruction verifies ZF (Zero Flag in FLAGS) and stops repetition when ZF=1.
Remember that ZF is set every time an arithmetical or logical operation result is 0.
Compare instructions (like CMPS, SCAS) set ZF if the operands are Equal.
REP repeats the instruction and decrements [E]CX n-times, where n is the initial content of [E]CX (at the end, [E]CX=0).
REPE/REPZ repeats the instruction and decrements [E]CX until [E]CX=0 or ZF=0.
REPNE/REPNZ repeats the instruction and decrements [E]CX until [E]CX=0 or ZF=1.

## Slide 6
no
[E]CX=0
Execute instruction
Increment/ decrement [E]SI and/or [E]DI by 1, 2 or 4
yes
next instruction
previous instruction
Decrement [E]CX by 1
ZF=1
[E]CX=0
Execute instruction
Increment/ decrement [E]SI and/or [E]DI by 1, 2 or 4
no
no
yes
yes
next instruction
previous instruction
Decrement [E]CX by 1
ZF=1
[E]CX=0
Execute instruction
Increment/ decrement [E]SI and/or [E]DI by 1, 2 or 4
no
no
yes
yes
next instruction
previous instruction
Decrement [E]CX by 1
3.7 String Instructions
The REP, REPE/REPZ, REPNE/REPNZ prefixes

## Slide 7
Example:
...
.DATA ;Data Segment
STRS DB `SHOPPER `,0DH ;declare a byte string
STRD DB 9 DUP (?) ; “
...
ASTRS DW OFFSET STRS,SEG STRS ;build in memory (Data Segment) the 4 byte
ASTRD DW OFFSET STRD,SEG STRD ;pointer to address STRS and STRD
.CODE
MOV AX,SEG ASTRS ;initializing DS for the segment of ASTRS
MOV DS,AX ;
…
CLD ;auto-increment SI and DI
MOV CX,7 ;initializing CX
…
LDS SI,ASTRS ;initialize DS and SI
LES DI,ASTRD ;initialize ES and DI (ES=DS in example)
MOVS STRD,STRS ;move an element from STRS to STRD
MOVSB ;move next element from STRS to STRD
REP MOVSB ;move next 7 elements from STRS to STRD
...
incrementing DI and SI but not decrementing CX
decrementing CX
3.7 String Instructions

## Slide 8
Example:
...
.DATA ;Data Segment
STRS DB `SHOPPER `,0DH ;declare a byte string
STRD DB `SHOPPING`,0DH ; “
.CODE
…
CLD ;auto-increment SI and DI
MOV CX, 8 ;initializing CX
…
MOV AX, SEG STRS ;initialize DS...
MOV DS, AX ;(in two steps)
MOV SI, OFFSET STRS ;...and SI.
MOV AX, SEG STRD ;initialize ES…
MOV ES, AX ;(ES=DS in example)
MOV DI, OFFSET STRD ;…and DI.
CMPSB ;compare first elements of STRS and STRD
REP CMPSB ;compare the next 8 bytes of the strings above
3.7 String Instructions