## Slide 1
Ambiguous: byte, word, double-word?
3.6 Data transfer Instructions
The MOV instruction
Examples:
MOV AL,30H
MOV AX,30H
Byte 30H is loaded into AL
Word 0030H is loaded into AX
BX  0028H
MOV [SI],0
MOV WORD PTR [SI],0
Word 0000H is loaded into memory at address [SI]
Only 386+
MOVSX BX,AL
MOVSX BX,AL
BX  FF91H
MOVZX BX,AL
BX  0091H
Supposing:
AL=28H
AL=91H
AL=91H

## Slide 2
3.6 Data transfer Instructions
The PUSH and POP instructions
Examples:
supposing:
DS=4000H
SS=0500H
SP=0300H
SI=0200H
AX=1234H
mem(40204H)=3FH
mem(40205H)=2FH
EBX=55AA66BBH
PUSHW SP
PUSHW [SI+4]
PUSHD EBX
...
...
PUSH AX
Initial
stack-top
…
POPD EBX
POPW [SI+4]
POPW SP
POP BX
...
(EBX)55AA66BBH
mem(40204H)  3FH
mem(40205H)  2FH
SP  2FEH
BX  1234H
Ph.Addr.=DS*10H+SI+4
STACK= LIFO list in memory, increasing toward 0.

## Slide 3
3.6 Data transfer Instructions
The PUSHA and POPA instructions
Examples:
supposing:
SS=0320H
SP=0800H
AX=00FFH
CX=EEDDH
DX=CCBBH
BX=AA99H
SP=0800H
BP=6655H
SI=4433H
DI=2211H
...
PUSHA
...
POPA order
PUSHA order
POPA
...

## Slide 4
3.6 Data transfer Instructions
The PUSHF, PUSHFD, POPF and POPFD instructions
It is not mandatory that a value pushed onto stack from a register (memory location) to be popped in the same register (memory location).
But it is a usual way to do so, using a sequence of PUSH instructions at a point in program, and a corresponding reversed sequence of POP instructions later.
The correct handling of the stack is the programmer’s responsibility.
CALL, INT and RET affect stack also.

## Slide 5
3.6 Data transfer Instructions
The IN instruction
Examples (DX=01FF):
IN AL,30H
IN AX,DX
A byte is read in AL from input port at address 0030H
A word is read in AX from input port at address 01FFH
Input port address can be expressed direct (8 bits) or register indirect using DX (16 bits).
The OUT instruction
Examples (DX=01FF):
OUT DX, AL
OUT 30H, AX
Output port address can be expressed direct (8 bits) or register indirect using DX (16 bits).
The source is always the accumulator. A byte can be output using AL, a word using AX or a double word using EAX.
The destination is always the accumulator. A byte can be input using AL, a word using AX, or a double word using EAX.
A byte is written from AL at output port at address 01FFH
A word is written from AX at output port at address 0030H

## Slide 6
3.6 Data transfer Instructions
The INS instruction
Input port address is always expressed register indirect using DX (16 bits).
The OUTS instruction
Output port address is always expressed register indirect using DX (16 bits).
The source is the memory location addressed by [E]SI. A byte, a word or a double word can be output. After output, [E]SI is automatically incremented (or decremented - depending on processor’s direction flag DF) by 1, 2 or 4.
The destination is the memory location addressed by ES:[E]DI. A byte, a word or a double word can be input. After input, [E]DI is automatically incremented (or decremented - depending on processor’s direction flag DF) by 1, 2 or 4.